## Slide 1: The Memory Hierarchy
CSCI 370 – Computer Architecture

## Slide 2: Today (and next week)
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 3: Random-Access Memory (RAM)
Key features
  RAM is traditionally packaged as a chip.
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
Static RAM (SRAM)
  Each cell stores a bit with a four or six-transistor circuit.
  Retains value indefinitely, as long as it is kept powered.
  Relatively insensitive to electrical noise (EMI), radiation, etc.
  Faster and more expensive than DRAM.
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor. One transistor is used for access
  Value must be refreshed every 10-100 ms.
  More sensitive to disturbances (EMI, radiation,…) than SRAM.
  Slower and cheaper than SRAM.

## Slide 4: SRAM vs DRAM Summary
Trans. Access Needs Needs
per bit time refresh? EDC? Cost Applications
SRAM 4 or 6 1X No Maybe 100x Cache memories
DRAM 1 10X Yes Yes 1X Main memories,
frame buffers

## Slide 5: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 6: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 7: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 8: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 9: Enhanced DRAMs
Basic DRAM cell has not changed since its invention in 1966.
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR4 (8 bits)
    By 2010, standard for most server and desktop systems

## Slide 10: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs with partial (sector) erase capability
    Wears out after about 100,000 erasings.
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
  Disk caches

## Slide 11: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 12: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%rax
Load operation: movq A, %rax

## Slide 13: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%rax
Load operation: movq A, %rax

## Slide 14: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %rax.
x
ALU
Register file
Bus interface
x
Main memory
0
A
%rax
I/O bridge
Load operation: movq A, %rax

## Slide 15: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
ALU
Register file
Bus interface
A
0
A
Main memory
I/O bridge
%rax y
Store operation: movq %rax, A

## Slide 16: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 17: Memory Write Transaction (3)
Main memory reads data word y from the bus and stores it at address A.

## Slide 18: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller.
  Converts requests for logical blocks into (surface,track,sector) triples.
Allows controller to set aside spare cylinders for each zone.
  Accounts for the difference in “formatted capacity” and “maximum capacity”.

## Slide 19: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 20: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 21: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 22: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 23: Solid State Disks (SSDs)
Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased
A block wears out after ~400,000 repeated writes.
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks

## Slide 24: SSD Performance Characteristics
Why are random writes so slow?
  Erasing a block is slow (around 1 ms)
  Write to a page triggers a copy of all useful pages in the block
    Find an used block (new block) and erase it
    Write the page into the new block
    Copy other pages from old block to the new block
Sequential read tput 2250 MB/s Sequential write tput 1870 MB/s
Random read tput 1140 MB/s Random write tput 104 MB/s
Rand read access 30 us Random write access 300 us

## Slide 25: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    E.g. Intel X25 guarantees 1 petabyte (1015 bytes) of random writes before they wear out
    More recent tests put leaders at over 20PB (20,000 TB!!!) of random writes
  $$$$
Applications
  MP3 players, smart phones, laptops
  desktops and servers
  Low energy applications

## Slide 26: Storage Trends
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 8,000 880 100 30 1 0.1 0.06 130,000
access (ns) 375 200 100 70 60 50 40 9
typical size (MB) 0.064 0.256 4 16 64 2,000 8,000 125,000
DRAM
SRAM
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 500 100 8 0.30 0.01 0.005 0.0003 1,600,000
access (ms) 87 75 28 10 8 4 3 29
typical size (MB) 1 10 160 1,000 20,000 160,000 1,500,000 1,500,000
Disk
Metric 1980 1985 1990 1995 2000 2005 2010 2010:1980
$/MB 19,200 2,900 320 256 100 75 60 320
access (ns) 300 150 35 15 3 2 1.5 200

## Slide 27: CPU Clock Rates
1980 1990 1995 2000 2003 2005 2010 2010:1980
CPU 8080 386 Pentium P-III P-4 Core 2 Core i7 ---
Clock
rate (MHz) 1 20 150 600 3300 2000 2500 2500
Cycle
time (ns) 1000 50 6 1.6 0.3 0.50 0.4 2500
Cores 1 1 1 1 1 2 4 4
Effective
cycle 1000 50 6 1.6 0.3 0.25 0.1 10,000
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”

## Slide 28: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1980 | 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010
Disk seek time | 87000000 | 75000000 | 28000000 | 10000000 | 8000000 | 8000000 | 8000000 | 8000000
Flash SSD access time | 75000
DRAM access time | 375 | 200 | 100 | 70 | 60 | 55 | 50 | 40
SRAM access time | 300 | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5
CPU cycle time | 1000 | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4
Effective CPU cycle time | 0.3 | 0.25 | 0.1
Disk
DRAM
CPU
SSD

## Slide 29: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 30: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 31: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 32: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 33: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 34: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 35: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 36: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 37: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 38: An Example Memory Hierarchy
Registers
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
Main memory holds disk blocks retrieved from local disks
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from L2 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
costlier
per byte
L3 cache
(SRAM)
L4 cache
(eDRAM) [emerging]
L3 cache holds cache lines retrieved from (L4 cache or) main memory

## Slide 39: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 40: For computers, memory accesses are like going to the library,

## Slide 41: Finding the necessary information in the page of a book,

## Slide 42: And going back home to do the work involving that information.

## Slide 43: While computers don‛t mind going back and forth like this for data, it usually means users have to do a lot of waiting.

## Slide 44: Fortunately for users, computers have caches, which is the equivalent of keeping copies of the books needed on a shelf near the workspace. Through a number of mechanisms, caches give the illusion of being able to access memory very quickly!

## Slide 45: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 46: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 47: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 48: Types of Cache Misses
Compulsory |  | Compulsory misses happen when a block is referenced for the first time. The computer can‛t get a block that doesn‛t exist yet!
Capacity |  | The block is not in the cache because there is no space in the cache for it. Caches are of finite size, after all.
Conflict |  | These types of misses happen only in direct-mapped and set- associative caches. Multiple blocks can be mapped to a set, forcing evictions when the set is full.

## Slide 49: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 50: Examples of Caching in the Hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
64-bytes block
64-bytes block
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
1
On-Chip L1
Hardware
10
On/Off-Chip L2
AFS/NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 51: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
  Hold frequently accessed blocks of main memory
CPU looks first for data in caches (e.g., L1, L2, and L3), then in main memory.
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memories

## Slide 52: Today
Caching in the memory hierarchy
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 53: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 54: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 55: Cache Associativity
t | index | offset
tag | index | offset
tag | i | offset
tag | offset
Direct Map
2-Way Set Associative
4-Way Set Associative
Fully Associative
A cache block can only go in one spot in the cache. It makes a cache block very easy to find, but it‛s not very flexible about where to put the blocks.
This cache is made up of sets that can fit two blocks each. The index is now used to find the set, and the tag helps find the block within the set.
Each set here fits four blocks, so there are fewer sets. As such, fewer index bits are needed.
No index is needed, since a cache block can go anywhere in the cache. Every tag must be compared when finding a block in the cache, but block placement is very flexible!

## Slide 56: Cache Associativity
All wonky images shamelessly purged from http://csillustrated.berkeley.edu/

## Slide 57: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 58: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 59: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
No match: old line is evicted and replaced

## Slide 60: Direct-Mapped Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 61: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_cols(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; i < 16; i++)
for (i = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 62: E-way Set Associative Cache
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 63: E-way Set Associative Cache
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 64: E-way Set Associative Cache
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 65: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 66: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 B = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; i < 16; i++)
for (i = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 67: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 68: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.

## Slide 69: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycle for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 70: Lets think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 71: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories.

## Slide 72: Today
Caching in the memory hierarchy
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 73: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (GB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 74: Memory Mountain Test Function
/* The test function */
void test(int elems, int stride) {
int i, result = 0;
volatile int sink;
for (i = 0; i < elems; i += stride)
result += data[i];
sink = result; /* So compiler doesn't optimize away the loop */
}
/* Run test(elems, stride) and return read throughput (MB/s) */
double run(int size, int stride, double Mhz)
{
double cycles;
int elems = size / sizeof(int);
test(elems, stride); /* warm up the cache */
cycles = fcyc2(test, elems, stride, 0); /* call test(elems,stride) */
return (size / stride) / (cycles / Mhz); /* convert cycles to MB/s */
}

## Slide 75: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip

## Slide 76: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality

## Slide 77: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
32 KB L1 i-cache
32 KB L1 d-cache
256 KB unified L2 cache
8M unified L3 cache
All caches on-chip
Slopes of
spatial
locality
Ridges of
Temporal
locality

## Slide 78: Memory Mountain (2009)
Intel Core i7 950
3.06GHz
Quad-core
Nehalem
32 KB L1I$
32 KB L1D$
256 KB unified L2$
8M unified L3$
24GB DDR3 @ 1333MHz

## Slide 79: Memory Mountain (2014)
Intel Core i7 5930K
3.50GHz
Hex-core
Haswell-E
32 KB L1I$
32 KB L1D$
256 KB unified L2$
15M unified L3$
32GB DDR4 @ 2133MHz
Notes: Talk about:
Bandwidth
LL$ change (order of magnitude change for datasize slope ~ 8M)
Similarities between the two

## Slide 80: Today
Caching in the memory hierarchy
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 81: Miss Rate Analysis for Matrix Multiply
Assume:
  Line size = 32B (big enough for four 64-bit words)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j

## Slide 82: Matrix Multiplication Example
Description:
Multiply N x N matrices
O(N3) total operations
N reads per source element
N values summed per destination
  but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
c[i][j] += a[i][k] *
b[k][j];
}
}
}

## Slide 83: Layout of C Arrays in Memory
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > 4 bytes, exploit spatial locality
    compulsory miss rate = 4 bytes / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    compulsory miss rate = 1 (i.e. 100%)

## Slide 84: Matrix Multiplication (i-j-k)
/* ijk */
for (i = 0; i < n; ++i) {
for (j = 0; j < n; ++j) {
sum = 0.0;
for (k = 0; k < n; ++k)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 85: Matrix Multiplication (j-i-k)
/* jik */
for (j = 0; j < n; ++j) {
for (i = 0; i < n; ++i) {
sum = 0.0;
for (k = 0; k < n; ++k)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 86: Matrix Multiplication (k-i-j)
(i,k)
/* kij */
for (k = 0; k < n; ++k) {
for (i = 0; i < n; ++i) {
r = a[i][k];
for (j = 0; j < n; ++j)
c[i][j] += r * b[k][j];
}
}
A
B
C
(k,*)
(i,*)
Inner loop:
Row-wise
Fixed
Row-wise
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 87: Matrix Multiplication (i-k-j)
(i,k)
/* ikj */
for (i = 0; i < n; ++i) {
for (k = 0; k < n; ++k) {
r = a[i][k];
for (j = 0; j < n; ++j)
c[i][j] += r * b[k][j];
}
}
A
B
C
(k,*)
(i,*)
Inner loop:
Row-wise
Fixed
Row-wise
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25

## Slide 88: Matrix Multiplication (j-k-i)
/* jki */
for (j = 0; j < n; ++j) {
for (k = 0; k < n; ++k) {
r = b[k][j];
for (i = 0; i < n; ++i)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,k)
(k,j)
(*,j)
Inner loop:
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0 1.0

## Slide 89: Matrix Multiplication (k-j-i)
/* kji */
for (k = 0; k < n; ++k) {
for (j = 0; j < n; ++j) {
r = b[k][j];
for (i = 0; i < n; ++i)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,k)
(k,j)
(*,j)
Inner loop:
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0 1.0

## Slide 90: Summary of Matrix Multiplication
i-j-k and j-i-k:
  2 loads, 0 stores
  misses/iter = 1.25
k-i-j and i-k-j:
  2 loads, 1 store
  misses/iter = 0.5
j-k-i and k-i-j:
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 91: Core i7 Matrix Multiply Performance
Chart: Matrix Size
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750
jki | 6.4 | 6.87 | 4.14 | 5.53 | 10.93 | 33.23 | 49.43 | 51.49 | 52.06 | 52.06 | 52.07 | 52.09 | 52.12 | 52.17 | 52.2
kji | 6.4 | 6.82 | 4.01 | 5.33 | 11.04 | 33.21 | 49.42 | 51.5 | 52.07 | 52.08 | 52.09 | 52.1 | 52.14 | 52.19 | 52.23
ijk | 5.31 | 6.35 | 6.29 | 3.7 | 3.72 | 3.71 | 3.72 | 3.83 | 4.6 | 7.74 | 11.71 | 16.54 | 20.57 | 23.85 | 23.86
jik | 5.4 | 6.23 | 3.64 | 3.71 | 3.61 | 3.6 | 3.63 | 3.74 | 4.64 | 7.57 | 11.62 | 16.44 | 20.44 | 23.68 | 23.66
kij | 4.37 | 5.36 | 3.23 | 3.32 | 3.29 | 3.24 | 3.2 | 3.17 | 3.16 | 3.14 | 3.13 | 3.12 | 3.1 | 3.1 | 3.08
ikj | 3.58 | 5.31 | 3.19 | 3.18 | 3.15 | 3.12 | 3.1 | 3.1 | 3.11 | 3.09 | 3.07 | 3.06 | 3.02 | 3.02 | 3.01
j-k-i / k-j-i
i-j-k / j-i-k
k-i-j / i-k-j

## Slide 92
Chart: Cache Miss Performance of Matrix Multiplication on Intel Core i7 950 (Nehalem)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750
i-j-k | 0.0003677 | 0.031534 | 0.031408 | 0.031363 | 0.031332 | 0.031323 | 0.032466 | 0.034949 | 0.084859 | 0.23601 | 0.43781 | 0.51679 | 0.53151 | 0.5314 | 0.53148
i-k-j | 0.00053922 | 0.068674 | 0.073687 | 0.09021 | 0.086553 | 0.086596 | 0.086621 | 0.094819 | 0.092024 | 0.091477 | 0.091032 | 0.096478 | 0.094331 | 0.093752 | 0.093255
j-i-k | 0.00022072 | 0.035702 | 0.034253 | 0.033511 | 0.033056 | 0.032763 | 0.032739 | 0.037061 | 0.074137 | 0.25719 | 0.4524 | 0.51788 | 0.53151 | 0.53149 | 0.53148
j-k-i | 0.00022072 | 0.035702 | 0.034253 | 0.033511 | 0.033056 | 0.032763 | 0.032739 | 0.037061 | 0.074137 | 0.25719 | 0.4524 | 0.51788 | 0.53151 | 0.53149 | 0.53148
k-i-j | 0.00013707 | 0.023495 | 0.022614 | 0.022175 | 0.021908 | 0.021731 | 0.021602 | 0.021507 | 0.021432 | 0.021373 | 0.021324 | 0.021283 | 0.021249 | 0.021219 | 0.021193
k-j-i | 0.00014593 | 0.020504 | 0.020619 | 0.023598 | 0.18827 | 0.60253 | 0.65412 | 0.66175 | 0.6623 | 0.66273 | 0.66309 | 0.66338 | 0.66364 | 0.66385 | 0.66404

## Slide 93
Chart: Cache Miss Performance of Matrix Multiplication on Intel Core i7 5930K (Haswell-E)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750
i-j-k | 0.00043687 | 0.03005 | 0.030403 | 0.030603 | 0.03072 | 0.030825 | 0.03266 | 0.037136 | 0.091118 | 0.24304 | 0.43824 | 0.51457 | 0.52898 | 0.52906 | 0.52928
i-k-j | 0.00090209 | 0.093871 | 0.10677 | 0.1148 | 0.12024 | 0.12419 | 0.12717 | 0.17447 | 0.16424 | 0.16256 | 0.16121 | 0.16011 | 0.15918 | 0.15839 | 0.15772
j-i-k | 0.00027969 | 0.034245 | 0.033291 | 0.032794 | 0.032487 | 0.032292 | 0.032448 | 0.038198 | 0.077484 | 0.25961 | 0.45067 | 0.515 | 0.52863 | 0.52882 | 0.52898
j-k-i | 0.00016803 | 0.023266 | 0.02249 | 0.028957 | 0.20348 | 0.6062 | 0.65523 | 0.66254 | 0.66299 | 0.66336 | 0.66366 | 0.66391 | 0.66412 | 0.6643 | 0.66446
k-i-j | 0.00017308 | 0.023051 | 0.022324 | 0.02196 | 0.021736 | 0.021589 | 0.021481 | 0.021401 | 0.021338 | 0.021289 | 0.021247 | 0.021213 | 0.021184 | 0.021159 | 0.021137
k-j-i | 0.00018592 | 0.020279 | 0.020472 | 0.026263 | 0.19825 | 0.6045 | 0.65428 | 0.66177 | 0.66231 | 0.66274 | 0.66309 | 0.66339 | 0.66364 | 0.66386 | 0.66404

## Slide 94: Core i7 5930K Timing
Chart: Performance of Various Loop Permutations
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
ijk | 88.2 | 606.4 | 3109.8 | 4917 | 9325.6 | 20205.4 | 33031.6 | 44659.6 | 68748 | 99001.2 | 147116.2 | 189472.2 | 253814 | 304865.2 | 388411.4 | 462174 | 569871 | 682234.6 | 913306.4 | 1156995.2
ikj | 34.8 | 187.8 | 905 | 1124.8 | 2416 | 4098.8 | 6465.4 | 8083 | 12501 | 16400 | 22914 | 25618.4 | 37255.2 | 45274.6 | 57071.8 | 58324 | 76893.2 | 90877.6 | 115153 | 124929.2
jik | 85 | 651.2 | 2253.2 | 4781.6 | 11135.2 | 17772 | 29551.4 | 43429.8 | 62048.8 | 92223 | 135468.6 | 182424.4 | 235534.2 | 292535.4 | 364134.4 | 453846.2 | 532536.8 | 650591.4 | 770772.4 | 1017083
jki | 92 | 708.8 | 2230.8 | 5802.6 | 17236.4 | 40618.8 | 87317.6 | 143071.2 | 198878.6 | 277107.4 | 365264.4 | 476980.8 | 611109.6 | 751826.8 | 2636299 | 5484314 | 6996036 | 9098113 | 11205195 | 13912894
kij | 96.6 | 681.8 | 2232 | 5407.2 | 10357.4 | 18169.6 | 27806.4 | 41364.8 | 59220.4 | 78716.2 | 106071.4 | 135049.6 | 173000.6 | 222173.2 | 265189.8 | 330705.6 | 402892.4 | 473125.2 | 603633.2 | 646121.4
kji | 95 | 679.4 | 2315.4 | 5830.4 | 15379.4 | 48914 | 91473.4 | 142854.4 | 203774.2 | 275241.6 | 367211.6 | 480081 | 611039 | 759937 | 2622023 | 5529613 | 7081599.5 | 8944705 | 11503641 | 13883397

## Slide 95: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 96: Example: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n+j] += a[i*n + k]*b[k*n + j];
}

## Slide 97: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 98: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 99: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B

## Slide 100: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks

## Slide 101: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 102: Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly

## Slide 103: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.
Programmer can optimize for cache performance
  Data organization, data access (blocking)
All systems favor “cache friendly code”
  Getting absolute optimum performance is very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)