## Slide 1: Floating Point and SIMD
CSCI 370 – Computer Architecture

## Slide 2: Background: IA-32 Floating Point
Floating Point Unit (X87 FPU)
  Hardware to +, -, *, and / IEEE floating point numbers
  8 80-bit registers organized as a stack (st0-st7)
  Operands pushed onto stack and operators can pop results off into memory
History
  8086: first CPU to implement IEEE FP
    separate 8087 FPU
  486: merged FPU and Integer Unit onto one chip
Instruction
decoder and
sequencer
FPU
Integer
Unit
Memory

## Slide 3: FPU Data Register Stack
FPU register format (extended precision)
s
exp
frac
0
63
64
78
79
FPU registers
  8 registers
  Logically forms shallow stack
  Top called %st(0)
  When push too many, bottom values disappear
stack grows down
“Top”
%st(0)
%st(1)
%st(2)
%st(3)

## Slide 4: Simplified FPU operation
“load” instruction
  Pushes number onto stack
“storep” instruction
  Pops top element from stack and stores it in memory
unary operation
  “neg” = pop top element, negate it, push result onto stack
binary operations
  “addp”, “multp” = pop top two elements, perform operation, push result onto stack
Stack operation similar to Reverse Polish Notation
  a b + = push a, push b, add

## Slide 5: Example calculation
x = (a - b) / (-b + c)
  load c
  load b
  neg
  addp
  load b
  load a
  subp
  divp
  storep x

## Slide 6: FPU instructions
Large number of floating point instructions and formats
  ~50 basic instruction types
  load (fld*), store (fst*), add (fadd), multiply (fmul)
  sin (fsin), cos (fcos), tan (ftan), etc.
Sample instructions:
Instruction Effect Description
fldz push 0.0 Load zero
flds Addr push M[Addr] Load single precision real
fmuls Addr %st(0) <- %st(0)*M[Addr] Multiply
faddp %st(1) <- %st(0)+%st(1); pop Add and pop
After pop, %st(0) has result

## Slide 7: FPU instruction mnemonics
Precision
  “s” single precision
  “l” double precision
Operand order
  Default Op1 <op> Op2
  “r” reverse operand order (i.e. Op2 <op> Op1)
Stack operation
  “p” pop a single value from stack upon completion

## Slide 8: Floating Point Code Example
Compute Inner Product of Two Vectors
  Single precision arithmetic
  Common computation
float ipf (float x[],
float y[],
int n)
{
int i;
float result = 0.0;
for (i = 0; i < n; i++) {
result += x[i] * y[i];
}
return result;
}
pushl %ebp # setup
movl %esp,%ebp
pushl %ebx
movl 8(%ebp),%ebx # %ebx=x
movl 12(%ebp),%ecx # %ecx=y
movl 16(%ebp),%edx # %edx=n
fldz # push +0.0
xorl %eax,%eax # i=0
cmpl %edx,%eax # if i>=n done
jge .L3
.L5:
flds (%ebx,%eax,4) # push x[i]
fmuls (%ecx,%eax,4) # st(0)*=y[i]
faddp # st(1)+=st(0); pop
incl %eax # i++
cmpl %edx,%eax # if i<n repeat
jl .L5
.L3:
movl -4(%ebp),%ebx # finish
movl %ebp, %esp
popl %ebp
ret # st(0) = result

## Slide 9: Inner Product Stack Trace
1. fldz
0.0
%st(0)
2. flds (%ebx,%eax,4)
0.0
%st(1)
x[0]
%st(0)
3. fmuls (%ecx,%eax,4)
0.0
%st(1)
x[0]*y[0]
%st(0)
4. faddp
x[0]*y[0]+0.0
%st(0)
5. flds (%ebx,%eax,4)
x[0]*y[0]
%st(1)
x[1]
%st(0)
6. fmuls (%ecx,%eax,4)
x[0]*y[0]
%st(1)
x[1]*y[1]
%st(0)
7. faddp
x[1]*y[1]+x[0]*y[0]
%st(0)
Initialization
Iteration 0
Iteration 1
Serial, sequential operation

## Slide 10: Motivation for SIMD
Multimedia, graphics, scientific, and security applications
  Require a single operation across large amounts of data
    Frame differencing for video encoding
    Image fade-in/fade-out
    Sprite overlay in game
    Matrix computations
    Encryption/decryption
  Algorithm characteristics
    Access data in a regular pattern
    Operate on short data types (8-bit, 16-bit, 32-bit)
    Have an operating paradigm that has data streaming through fixed processing stages

## Slide 11: Natural fit for SIMD instructions
Single Instruction, Multiple Data
  Also known as vector instructions
  Before SIMD
    One instruction per data location
  With SIMD
    One instruction over multiple sequential data locations
    Execution units must support “wide” parallel execution
Examples in many processors
  Intel x86
    MMX, SSE, AVX, AVX2, AVX-512
  ARM
    Neon (128-bit)

## Slide 12: Example
R = R + XR * 1.08327
G = G + XG * 1.89234
B = B + XB * 1.29835
R R XR 1.08327
G = G + XG * 1.89234
B B XB 1.29835
R = R + X[i+0]
G = G + X[i+1]
B = B + X[i+2]
R R
G = G + X[i:i+2]
B B

## Slide 13: Example
for (i=0; i<64; i+=4)‏
A[i:i+3] = A[i:i+3] + B[i:i+3]
for (i=0; i<64; i+=4)‏{
A[i+0] = A[i+0] + B[i+0]
A[i+1] = A[i+1] + B[i+1]
A[i+2] = A[i+2] + B[i+2]
A[i+3] = A[i+3] + B[i+3]
}
for (i=0; i<64; i+=1)‏
A[i+0] = A[i+0] + B[i+0]

## Slide 14: SIMD in x86
MMX (MultiMedia eXtensions)
  Pentium, Pentium II
SSE (Streaming SIMD Extensions) (1999)
  Pentium 3
SSE2 (2000), SSE3 (2004)
  Pentium 4
SSSE3 (2004), SSE4 (2007)
  Intel Core
AVX (2011)
  Intel Sandy Bridge
AVX2 (2013)
  Intel Haswell
AVX-512 (2016)
  Intel Skylake-E

## Slide 15
General idea
SIMD (single-instruction, multiple data)
  Vector instructions
  New data types, registers, operations
  Parallel operation on small (length 2-8) vectors of integers or floats
  Example:
+
x
“4-way”
Notes: 15

## Slide 16: MMX (MultiMedia eXtensions)
MMX re-uses FPU registers for SIMD execution of integer ops
  Alias the FPU registers st0-st7 as MM0-MM7
  Treat as 8 64-bit data registers randomly accessible
  Partition registers based on data type of vector
  How many different partitions are there for a vectored add?
  Single operation applied in parallel on individual parts
Why not new registers?
  Wanted to avoid adding CPU state
    Change does not impact context switching
    OS does not need to know about MMX
  Drawback: can't use FPU and MMX at the same time
8 byte additions (PADDB)
4 short or word additions (PADDW)
2 int or dword additions (PADDD)
+
+
+

## Slide 17
SSE3 Registers
All caller saved
%xmm0 for floating point return value
%xmm0
%xmm1
%xmm2
%xmm3
%xmm4
%xmm5
%xmm6
%xmm7
%xmm8
%xmm9
%xmm10
%xmm11
%xmm12
%xmm13
%xmm14
%xmm15
Argument #1
Argument #2
Argument #3
Argument #4
Argument #5
Argument #6
Argument #7
Argument #8
128 bit
Notes: 17

## Slide 18
SSE3 Registers
Different data types and associated instructions
Integer vectors:
  16-way byte
  8-way short
  4-way int
Floating point vectors:
  4-way single (float)
  2-way double
Floating point scalars:
  single
  double
128 bit
LSB
Notes: 18

## Slide 19
SSE3 Instruction Names
addps
addss
addpd
addsd
packed (vector)
single slot (scalar)
single precision
double precision
Notes: 19

## Slide 20
SSE3 Instructions: Examples
Single precision 4-way vector add: addps %xmm0 %xmm1
Single precision scalar add: addss %xmm0 %xmm1
+
%xmm0
%xmm1
+
%xmm0
%xmm1
Notes: 20

## Slide 21
SSE3 Basic Instructions
Moves
  Usual operand form: reg → reg, reg → mem, mem → reg
  Packed versions to load vector from memory
Arithmetic
Single | Double | Effect
addss | addsd | D ← D + S
subss | subsd | D ← D – S
mulss | mulsd | D ← D x S
divss | divsd | D ← D / S
maxss | maxsd | D ← max(D,S)
minss | minsd | D ← min(D,S)
sqrtss | sqrtsd | D ← sqrt(S)
Single | Double | Effect
movss | movsd | D ← S
Notes: 21

## Slide 22
x86-64 FP Code Example
Compute inner product of two vectors
  Single precision arithmetic
  Uses SSE3 instructions
float ipf (float x[],
float y[],
int n) {
int i;
float result = 0.0;
for (i = 0; i < n; i++)
result += x[i]*y[i];
return result;
}
ipf:
xorps %xmm1, %xmm1 # result = 0.0
xorl %ecx, %ecx # i = 0
jmp .L8 # goto middle
.L10: # loop:
movslq %ecx,%rax # icpy = i
incl %ecx # i++
movss (%rsi,%rax,4), %xmm0 # t = y[icpy]
mulss (%rdi,%rax,4), %xmm0 # t *= x[icpy]
addss %xmm0, %xmm1 # result += t
.L8: # middle:
cmpl %edx, %ecx # i:n
jl .L10 # if < goto loop
movaps %xmm1, %xmm0 # return result
ret

## Slide 23
SSE3 Conversion Instructions
Conversions
  Same operand forms as moves
Instruction | Description
cvtss2sd | single → double
cvtsd2ss | double → single
cvtsi2ss | int → single
cvtsi2sd | int → double
cvtsi2ssq | quad int → single
cvtsi2sdq | quad int → double
cvttss2si | single → int (truncation)
cvttsd2si | double → int (truncation)
cvttss2siq | single → quad int (truncation)
cvttss2siq | double → quad int (truncation)
Notes: 23

## Slide 24: Detecting Support for MMX and SSE
  mov 1, eax
  cpuid ; supported since Pentium
  test 0x800000, edx ; 00800000h (bit 23) MMX
  ; 02000000h (bit 25) SSE
  ; 04000000h (bit 26) SSE2
  jnz HasMMX

## Slide 25: Detecting Support (Cont’d)
  #include <stdio.h>
  #include <string.h>
  #define cpuid(func,ax,bx,cx,dx)\
  __asm__ __volatile__ ("cpuid":\
  "=a" (ax), "=b" (bx), "=c" (cx), "=d" (dx) : "a" (func));
  int main (int argc, char* argv[]) { int a, b, c, d, i; char s[13]; int* q; for (i = 0; i < 13; i++) s[i] = 0; q = (int *) s; /* 12 char string returned in 3 registers */ cpuid (0, a, q[0], q[2], q[1]); printf ("str: %s\n", s); /* Bits returned in all 4 registers */ cpuid (1, a, b, c, d); printf ("a: %08x, b: %08x, c: %08x, d: %08x\n", a, b, c, d); printf (" bh * 8 = cache line size\n"); printf (" bit 0 of c = SSE3 supported\n"); printf (" bit 25 of c = AES supported\n"); printf (" bit 0 of d = On-board FPU\n"); printf (" bit 4 of d = Time-stamp counter\n"); printf (" bit 26 of d = SSE2 supported\n"); printf (" bit 25 of d = SSE supported\n"); printf (" bit 23 of d = MMX supported\n");
  }

## Slide 26: Detecting Support (Cont’d)
% cat /proc/cpuinfo
processor : 0
vendor_id : GenuineIntel
cpu family : 6
model : 15
model name : Intel(R) Core(TM)2 Quad CPU Q6600 @ 2.40GHz
stepping : 11
cpu MHz : 2393.974
cache size : 4096 KB
physical id : 0
siblings : 4
core id : 0
cpu cores : 4
apicid : 0
initial apicid : 0
fpu : yes
fpu_exception : yes
cpuid level : 10
wp : yes
flags : fpu vme de pse tsc msr pae mce cx8 apic sep mtrr pge mca cmov pat pse36 clflush dts acpi mmx fxsr sse sse2 ss ht tm pbe syscall nx lm constant_tsc arch_perfmon pebs bts rep_good pni monitor ds_cpl vmx est tm2 ssse3 cx16 xtpr lahf_lm
bogomips : 4791.08
clflush size : 64
cache_alignment : 64
address sizes : 36 bits physical, 48 bits virtual
power management:

## Slide 27: AVX
Advanced Vector Extensions
Sandy Bridge (2011)
256-bit registers YMM0 – YMM15
AVX2
Intel codename Haswell (2013)
Expansion of most integer AVX to 256 bits
“Gather support” to load data from non-contiguous memory
3-operand FMA operations (fused multiply-add operations) at full precision (a+b*c)
  Dot products, matrix multiplications, polynomial evaluations via Horner's rule (see DEC VAX POLY instruction 1977)
  Speeds up software-based division and square root operations (so dedicated hardware for these operations can be removed)
AVX-512
512-bit extensions to AVX
Knights Landing (2016)
Skylake-E (2016)
Icelake (2019)
Register names ZMM0 – ZMM31

## Slide 28: Programming SIMD
Store data contiguously (i.e. in an array)
Define total size of vector in bytes
  8 bytes (64 bits) for MMX
  16 bytes (128 bits) for SSE2 and beyond
Define type of vector elements
  For 128 bit registers
    2 double
    4 float
    4 int
    8 short
    16 char
  SIMD instructions based on each vector type

## Slide 29
Vectorizing Code
Starting with version 4.1.1, gcc can autovectorize to some extent
  -O3 or –ftree-vectorize
  No speed-up guaranteed
  Very limited
  icc is often much better
For highest performance vectorize yourself using intrinsics
  Intrinsics = C interface to vector instructions
  https://software.intel.com/sites/landingpage/IntrinsicsGuide/
Notes: 29

## Slide 30
Architecture | Latency | Throughput
Haswell | 3 | 1
Ivy Bridge | 3 | 1
Sandy Bridge | 3 | 1
Westmere | 3 | 1
Nehalem | 3 | 1
Synopsis
__m128 _mm_add_ps (__m128 a, __m128 b)
#include "xmmintrin.h"
Instruction: addps xmm, xmm
CPUID Flags: SSE
Description
Add packed single-precision (32-bit) FP
elements in a and b, and store the results in dst.
Performance
Operation
FOR j := 0 to 3
i := j*32
dst[i+31:i] := a[i+31:i] + b[i+31:i]
ENDFOR
Intrinsics Functions