## Slide 1: Multicore and Thread-level Parallelism
CSCI 370 – Computer Architecture

## Slide 2: Architecture Considerations with Multicore
Cache
Execution Units
Anything else?
Notes: Out of order execution

## Slide 3: False Sharing
Coherency maintained on cache blocks
To update psum[i], thread i must have exclusive access
  Threads sharing common cache block will keep fighting each other for access to block
0
1
2
3
4
5
6
7
Cache Block m
Cache Block m+1
psum

## Slide 4: False Sharing Performance
  Best spaced-apart performance 2.8 X better than best adjacent
Demonstrates cache block size = 64
  8-byte values
  No benefit increasing spacing beyond 8

## Slide 5: Cache Coherency
A problem even on hierarchical architectures
Processor A writes location X
Processor B reads location X
What value does Processor B get? Before or after the write of A?

## Slide 6: Multicore Processor
Intel Nehalem (and newer) Processor
  Multiple processors operating with coherent view of memory
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core n-1
…
L3 unified cache
(shared by all cores)
Main memory

## Slide 8: Memory Consistency
What are the possible values printed?
  Depends on memory consistency model
  Abstract model of how hardware handles concurrent accesses
Sequential consistency
  Overall effect consistent with each individual thread
  Otherwise, arbitrary interleaving
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
Wa
Rb
Wb
Ra
Thread consistency
constraints

## Slide 9: Sequential Consistency Example
Impossible outputs
  100, 1 and 1, 100
  Would require reaching both Ra and Rb before Wa and Wb
Wa
Rb
Wb
Ra
Wb
Rb
Ra
Ra
Rb
Wb
Ra
Wa
Rb
Wa
Ra
Rb
Rb
Ra
100, 2
200, 2
2, 200
1, 200
2, 200
200, 2
Wa
Rb
Wb
Ra
Thread consistency
constraints
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 10: Non-Coherent Cache Scenario
Write-back caches, without coordination between them
Main Memory
a:1
b:100
Thread1 Cache
a: 2
Thread2 Cache
b:200
a:1
print 1
b:100
print 100
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 11: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
a: 2
E
b:200
E
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 12: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
a: 2
E
b:200
E
print 200
b:200
S
b:200
S
print 2
a:2
S
a: 2
S
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
When cache sees request for one of its E-tagged blocks
  Supply value from cache
  Set tag to S

## Slide 13: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
print 200
b:200
S
b:200
S
print 2
a:2
S
a: 2
S
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Wa: a = 3;
Thread2:
Wb: b = 200;
Ra: print(a);
Wb: b = 300;
When cache sees write for one of its S-tagged blocks
  Mark other cache’s tag to I
  Set tag to E
  update value
a:2
I
a: 3
E
b:200
I
b:300
E

## Slide 14: Out-of-Order Processor Structure
Instruction control dynamically converts program into stream of operations
Operations mapped onto functional units to execute in parallel
Functional Units
Integer
Arith
Integer
Arith
FP
Arith
Load /
Store
Instruction Control
Registers
Instruction Decoder
Op. Queue
Data Cache
Instruction
Cache
PC

## Slide 15: Hyperthreading
Replicate enough instruction control to process K instruction streams
K copies of all registers
Share functional units
Functional Units
Integer
Arith
Integer
Arith
FP
Arith
Load /
Store
Instruction Control
Reg B
Instruction Decoder
Op. Queue B
Data Cache
Instruction
Cache
Reg A
Op. Queue A
PC A
PC B

## Slide 16: A Visual Guide to Hyper-Threading

## Slide 17: A Visual Guide to Hyper-Threading

## Slide 18: Summary: Creating Parallel Machines
Multicore
  Separate instruction logic and functional units
  Some shared, some private caches
  Must implement cache coherency
Hyperthreading
  Also called “simultaneous multithreading” (SMT)
  Separate program state
  Shared functional units & caches
  No special control needed for coherency
Combining
  Theoretical speedup of cores * hyperthreads over sequential

## Slide 19: A More Interesting Example
Sort set of N random numbers
Multiple possible algorithms

## Slide 20: A More Interesting Example
Sort set of N random numbers
Sequential quicksort of set of values [X]
  Choose “pivot” p from [X]
  Rearrange [X] into
    [L] : values <=p
    [R] : values >p
  Recursively sort [L] to get [L’]
  Recursively sort [R] to get [R’]
  Return [L’] + [R’]
What can be done independently?

## Slide 21: Case Study: Quicksort
void quickSort(long int arr[], int left, int right) {
if (right – left <= 10) {
insertionSort(arr, left, right);
return;
}
int pivot = arr[(left + right) / 2];
int i = left;
int j = right;
partition (arr, &i, &j, pivot);
quickSort(arr, left, j);
quickSort(arr, i, right);
}

## Slide 22: Parallel Quicksort Performance
Sort 237 (134,217,728) random values
Best speedup = 6.84X

## Slide 23: Parallel Quicksort Performance
Good performance over wide range of fraction values
  F too small: Not enough parallelism
  F too large: Thread overhead + run out of thread memory