## Slide 1: Parallel Architectures
CSCI 476: Parallel Programming

## Slide 2: Hardware Parallelism
Computing: execute instructions that operate on data.
Flynn’s taxonomy (Michael Flynn, 1967) classifies computer architectures based on the number of instructions that can be executed and how they operate on data.
Computer
Instructions
Data

## Slide 3: Flynn’s taxonomy
Single Instruction Single Data (SISD)
  Traditional sequential computing systems
Single Instruction Multiple Data (SIMD)
Multiple Instructions Multiple Data (MIMD)
Multiple Instructions Single Data (MISD)
Computer Architectures
SISD
SIMD
MIMD
MISD

## Slide 4: SISD
At one time, one instruction operates on one data
Traditional sequential architecture

## Slide 5: SIMD
At one time, one instruction operates on many data
  Data parallel architecture
  Vector architecture has similar characteristics, but achieve the parallelism with pipelining.
Array processors

## Slide 6: Array processor (SIMD)
IP
MAR
MEMORY
MDR
ADDR
OP
DECODER
A1
B1
C1
A2
B2
C2
AN
BN
CN
ALU
ALU
ALU

## Slide 7: MIMD
Multiple instruction streams operating on multiple data streams
  Classical distributed memory or SMP architectures

## Slide 8: MISD machine
Not commonly seen.
Systolic array is one example of an MISD architecture.

## Slide 9: Flynn’s taxonomy summary
SISD: traditional sequential architecture
SIMD: processor arrays, vector processor
  Parallel computing on a budget – reduced control unit cost
  Many early supercomputers
MIMD: most general purpose parallel computer today
  Clusters, MPP, data centers
MISD: not a general purpose architecture.

## Slide 10: Flynn’s classification on today’s architectures
Multicore processors
Superscalar: Pipelined + multiple issues.
SSE (Intel and AMD’s support for performing operation on 2 doubles or 4 floats simultaneously).
  Now can handle 512-bits at a time
GPU: CUDA architecture
IBM BlueGene

## Slide 11: Modern Classification
Classify based on how parallelism is achieved
  by operating on multiple data: data parallelism
  by performing many functions in parallel: function parallelism
    Control parallelism, task parallelism depending on the level of the functional parallelism.
Parallel architectures
Data-parallel
architectures
Function-parallel
architectures

## Slide 12: Data parallel architectures
Vector processors, SIMD (array processors), systolic arrays.
IP
MAR
MEMORY
MDR
ADDR
OP
DECODER
A
B
C
ALU
Vector processor (pipelining)

## Slide 13
Data parallel architecture: Array processor
IP
MAR
MEMORY
MDR
ADDR
OP
DECODER
A1
B1
C1
A2
B2
C2
AN
BN
CN
ALU
ALU
ALU

## Slide 14: Control parallel architectures
Function-parallel architectures
Instruction level Parallel Arch
Thread level Parallel Arch
Process level Parallel Arch
(ILPs)
(MIMDs)
VLIWs
Superscalar processors
Distributed Memory MIMD
Shared Memory MIMD
Pipelined processors

## Slide 15: Classifying today’s architectures
Multicore processors?
Superscalar?
SSE?
GPUs?
ARM + X?

## Slide 16: Performance of parallel architectures
Common metrics
  MIPS: million instructions per second
    MIPS = instruction count/(execution time x 106)
  MFLOPS: million floating point operations per second.
    MFLOPS = FP ops in program/(execution time x 106)
Which is a better metric?
    FLOP is more related to the time of a task in numerical code
      # of FLOP / program is determined by the matrix size

## Slide 17: Performance of parallel architectures
    FlOPS units
      kiloFLOPS (KFLOPS) 10^3
      megaFLOPS (MFLOPS) 10^6
      gigaFLOPS (GFLOPS) 10^9  single CPU performance
      teraFLOPS (TFLOPS) 10^12
      petaFLOPS (PFLOPS) 10^15  we are here right now
        150 petaFLOPS supercomputers
      exaFLOPS (EFLOPS) 10^18  the next milestone

## Slide 18: Peak and sustained performance
Peak performance
  Measured in MFLOPS
  Highest possible MFLOPS when the system does nothing but numerical computation
  Rough hardware measure
  Little indication on how the system will perform in practice.

## Slide 19: Measuring the performance of parallel computers
Benchmarks: programs that are used to measure the performance.
  LINPACK benchmark: a measure of a system’s floating point computing power
    Solving a dense N by N system of linear equations Ax=b
    Use to rank supercomputers in the top500 list.

## Slide 20: LINPACK: Peak & Sustained Perf.

## Slide 21: High-Performance Conjugate Gradient

## Slide 22: Other common benchmarks
Micro benchmarks suit
  Numerical computing
    LAPACK
    ScaLAPACK
  Memory bandwidth
    STREAM
Kernel benchmarks
  NPB (NAS parallel benchmark)
  PARKBENCH
  SPEC
  Splash

## Slide 23: Summary
Flynn’s classification
  SISD, SIMD, MIMD, MISD
Modern classification
  Data parallelism
  function parallelism
    Instruction level, thread level, and process level
Performance
  MIPS, MFLOPS
  Peak performance and sustained performance